## Slide 1: Statistics for Soil Survey

## Slide 2: Pre-course Questionnaire
Where do you work ?
Years of Service –
Workload –
Statistics used –
  Mapping methods -
  Software -

## Slide 3: Pre-course Questionnaire: What You Want From this Course
  Become more familiar with R
  Exposure to statistics
  Learn how to analyze data efficiently
  Digital soil mapping applications
  Learn useful tools for PESD development, clustering pedons, and data aggregation
  Learn how to apply statistical methods within the realm of soil survey and its implications on soil survey standards

## Slide 4: Course Objectives
Develop solutions to investigate soil survey correlation problems and update activities.
Evaluate investigations for interpretive results and determine how to proceed.
Create a continuous surface from point data.
Summarize data for populations in NASIS.
Help to pursue the question “why”

## Slide 5: Overview: Why Is This Training Needed?
      Long standing goal of the Soil Science Division to have a course in statistics
      Opportunities to learn these techniques are limited, especially at the undergraduate level
      Consistent methodology (data analysis, data population, sampling design, etc.)
      There is continually a greater need to use these techniques:
        Mapping of lands at high production rates
        Ecological Sites
        Soil survey refinement (disaggregation)
Notes: Need identified about 10 years ago. Alignment of software and staff are available now.

## Slide 6: Overview: Why is course organized this way?
      Our best judgement for assembling into 24 hours what could be 6 University level courses
      Mixture of slides and script enabled web pages is new for NRCS
      The web content is a long-term investment and should serve as a permanent reference
      Feel free to provide guidance for improving the class for future offerings

## Slide 7: Overview: Week 1
Day 1
Introduction
Data We Use
Day 2
Data We Use
Sampling Design
Day 3
Exploratory Data Analysis
Clustering and Ordination
These are general guidelines

## Slide 8: Overview: Week 2
Day 4
Week 1 Review
Clustering and Ordination
Validation and Uncertainty
Linear Regression
Day 5
Linear Regression
Logistic Regression
Day 6
Tree Models
Final Project

## Slide 9: Final Project
Objective(s) - Describe what you will investigate and the methods that will be employed
Project Domain – could be confined to analysis of point data or horizons from KSSL or field descriptions, or include spatial component and resulting predictions
Results - Describe results using descriptive and graphical techniques. If predictions are used, include these
Discussion - Discuss how these results: 1) help in understanding the problem and 2) influence current and future investigations
Due date – March 24th, 2017

## Slide 10: Pre-course Assignment: History of NASIS
Notes: In Paul’s Youtube lecture, he discussed the difference between estimated and analyzed soil properties and presented an example of the importance of site selection. We as soil scientists have to extrapolate knowledge gained from a small set of point data to very large, unseen areas.

## Slide 11: Pre-course Assignment: History of NASIS
Notes: You should only populate NASIS with the lowest level of certainty, which is your field estimates. Do not populate NASIS with decimal points (lab precision/accuracy).

## Slide 12: Pre-course Assignment: RStudio
  In the pre-course assignment you:
  Set your working directory and verified the RStudio version
  Installed packages
  Established an open database connection (ODBC) to NASIS
  Ran fetchNASIS on a selected set

## Slide 13: Introduction to R
R Console:
R code is typed here when it is ready to be executed.
R Editor:
R code is typed here when it is in the process of being edited (you can also use notepad, notepad ++, etc.).
R Graphics:
Graphics are displayed in this window after plot() or another graphics function is executed in R Console.
Notes: There are two R that have been installed on your machine: R and RStudio. Both programs are command line driven and allow graphical display.
There are three main windows in R that you can use to conduct your data analysis: R Console, R Editor, and R Graphics. The R Editor window is simply a text editing window, you may also use notepad or notepad ++. The R Graphics window will only display when a command such as plot ( ) is executed.

## Slide 14: RStudio
Notes: RStudio is similar to R GUI, but is more user friendly. When you open RStudio on your machine, you will see 3 windows: the console window, just like in the R GUI and two other windows composed of multiple tabs. The upper right window has two tabs: environment and history. The environment tab will allow you to import data and keep track of the data objects you create in R. The history tab keeps a record of all the commands that you execute. The bottom right window has 5 tabs: files, plots, packages, help, and viewer. The files tab allows you to navigate through folders similar to windows explorer. The plots tab will display and keep track of all of the plots that you generate. The packages tab allows you to install, load, and update packages using a GUI. The help tab allows you to search for documentation on R commands or packages. Unlike google, it will not allow you to search for things like cat sweaters or how to tie a tie. The viewer tab is for more advanced R users. We will not discuss it in this course.

## Slide 15: RStudio
Notes: You can easily import data using the Environment tab.

## Slide 16: RStudio
Notes: If you click import dataset, an import window similar to excel will appear.

## Slide 17: RStudio
Notes: The text editor window, similar to R, can be opened in RStudio using the File drop down menu.

## Slide 18: RStudio
Notes: It is recommended to use the text editor window to develop your code before executing it in the console window.

## Slide 19: RStudio
Notes: At the beginning of each R session, whether you are using R or RStudio, you want to make sure that you set your working directory. This directory should be where your input datasets are stored, R files are located, and will also serve as the default storage of plots or exported objects from R. To do this in RStudio, simply use the Session drop down menu. Notice that once you set your working directory, the Files tab in the bottom right window navigates to the directory that you specified, in this example, a folder called R on the C drive.

## Slide 20: RStudio
Notes: R can be used as a calculator to solve simplistic mathematical equations like the one currently displayed, as a GIS, for statistical analysis, for sampling design, and for modeling. In order to execute the equation that I have typed, I must place my cursor on line 1 or highlight line 1 and select the Run button.
-Click-
Notice that the answer to my equation is displayed in the console window in the bottom left and the command is added to the History tab.

## Slide 21: RStudio - Objects
object <- function
object = function
Notes: In R you can assign almost anything as an object, including a single number or letter, model, settings, or dataset. For example, say I wanted to create an object entitled x that displayed rock fragment content of 3 different sites. I could do this in R by typing, x equals the concatenate function that links together the rock fragment values of 2, 4, and 6. Objects are displayed in the Environment tab in the upper right corner. In order to create an object in R, you must use either the = sign or a less than with a dash, either is fine. It is personal preference.
-Click-
Let’s create an object called clay to represent the clay content at these three sites.

## Slide 22: RStudio
Notes: Say we wanted to know the mean of our rock fragment content. The function for mean is conveniently mean in R, so you would type mean with x (our rock fragment dataset) in parenthesis.
-Click-
Once you run this command, the answer is displayed in the console as 4 and the function is added to the R history tab. When you type a function in RStudio, a drop down menu will open that will list all available functions with the term that you type.

## Slide 23: RStudio
Notes: What if I wanted to view the distribution of clay content? What function would I use? If I was unsure, I could use the Help tab in the bottom right and search for histogram.
-Click-
If I click on the graphics: hist link, a webpage describing the hist function appears.
-Click-
If I execute the hist command for clay content, you can see that a plot is generated in the plot tab in the bottom right.

## Slide 24: RStudio – Installing Packages
Notes: One thing that I have yet to mention is that both R programs are equipped with base packages that contain functions such as hist and mean. Packages are simply collections of code developed by R users. There are currently over 7,300 packages developed for use in R. For user convenience, RStudio developed a Packages tab in the lower right window that lists all of the packages that have been installed. In order to utilize these packages, the user must load them either by using the library() function or by checking the box next to the package name in the Packages tab.

## Slide 25
RStudio – Installing Packages
Notes: It may be necessary to install several packages that are not listed under the Packages tab. With no packages selected, click on Install under the Packages tab. In the packages text line, we will type four packages that have been used for soil survey applications, the aqp, sharpshootR, soilDB, and RODBC packages. Packages only need to be installed the first time you use them on your machine.
-Click-
Notice that the packages that we have installed depend and utilize many other packages that were also installed on our machine. It is important to always check the install dependencies box when installing a package in R.
AQP – visualization, aggregation, classification
soilDB – access to commonly used soil databases
SharpshootR – misc. soil survey specific functions
RODBC - ODBC Database Access

## Slide 26
RStudio – Installing Packages
Notes: Once installed, the packages are added to the Package tab in the bottom right corner. You can update packages when necessary by clicking on the Update icon in the Packages tab. Updates are available fairly often depending on the package, so it is important to keep packages updated. Every time you open RStudio, you will need to load the packages that you are going to use during your R session by checking the box next to the package name.
All packages in R are required to meet certain standards set by The Comprehensive R Archive Network, including documentation, sample datasets, and examples. Once you find a package that will accommodate the functions that you wish to run, it is simply a matter of reading the documentation and viewing the examples to understand how to apply the function to your data. Since R is an open source program, there are a TON of resources available online.

## Slide 27
RStudio – Installing Packages
Notes: You can also install and update packages using the Tools drop down menu.

## Slide 28: Pre-course Assignment: Open Database Connection (ODBC)
Links a local NASIS database to R so that pedon and DMU records can be queried with the soilDB package in RStudio.
Only needs to be done once on your machine.
Suggested NASIS queries to run:
  Pangaea query POINT - Pedon/Site/Transect by Current Taxon Name. This accepts a Taxon Name, for example, Gauley.
  Pangea query POINT - Pedon/Site by Correlated Name.
  Pangea query POINT - Pedon/Site/Transects by User Pedon ID (2100 Max).This accepts a comma delimited list, for example, 95IL151005E, 94IL153001, 95IL153001, 92IL163017.
  Pangea query POINT - Pedon/Site/Transects by Pedon Rec ID (2100 Max).This accepts a comma delimited list, for example, 44249, 175077, 101806, 44411.
  Pangea query POINT - PedonHorizon/Site/Transect by HorizonRecID (2100 Max). This accepts a comma delimited list, for example, 210618, 210619, 853291, 208951.
Notes: In order to fetch data from NASIS, data must first be in your selected set. The NASIS queries displayed above are suggested by Tom and Stephen for loading data into your selected set.

## Slide 29: EXERCISE
https://github.com/ncss-tech/stats_for_soil_survey/blob/master/chapters/1_introduction/1_introduction.md
Notes: Let's take a 10 minute break and then we will run through some introductory examples in R.